Preparação Teste
- Flip flop
- Registrador
- Contador
- Maquina com contador em memória
- Maquina com porta
- Maquina em memória para controle (elevador)
- Maquina para memória cache

---
Máquina com Contador
Contador para sequencia 0,2,0,3,0,2,0,3...
solução 4 estados
0
1
2
3

---
Máquina com Contador
Contador para sequencia 0,2,0,3,0,2,0,3...
solução 4 estados
0 = 00 tudo desligado
2 = 10 liga motor sobe
0 = 00 desliga
3 = 11 liga motor e desce

---
Máquina com Contador
Estado Proximo Saida
0 1 0
1 2 2
2 3 0
3 0 3

---
Máquina com Contador
Estado Proximo Saida
0 1=01 0=00
1 2=10 2=10
2 3=11 0=00
3 0=00 3=11
4 bits
2 bits para proximo
2 bits para saida
Estado Proximo Saida
0 01 00 =4
1 10 10 =A
2 11 00 =C
3 00 11 =3

---
Máquina com Contador
Estado Proximo Saida
0 01 00 =4
1 10 10 =A
2 11 00 =C
3 00 11 =3
4 bits
2 bits para proximo
2 bits para saida
FF
saida
proximo

---
ROM em VHDL
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.Numeric_Std.all;
entity rom_contador1 is
  port (address : in std_logic_vector (1 downto 0);
        data : out std_logic_vector (3 downto 0));
end entity rom_contador1;
architecture fsmrom of rom_contador1 is
  type rom_array is array (0 to 3) of std_logic_vector(3 downto 0);
  constant rom : rom_array := ("0100",
        "1010",
        "1100",
        "0011"
        );
begin
  data <= rom(to_integer(unsigned(address)));
end architecture fsmrom;

---
Usando a ROM com FSM
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
library work;
use work.ALL;
use IEEE.Numeric_Std.all;
entity fsm_contador1 is
port ( clk : in std_logic;
count : out std_logic_vector(1 downto 0));
end fsm_contador1;
architecture Behavioral of fsm_contador1 is
signal address : std_logic_vector(1 downto 0);
signal data : std_logic_vector(3 downto 0);
begin
rom : entity work.rom_contador1 port map(address,data);
fsmMemory : process(clk)
  begin
if (clk = '1' and clk'event) then
address <= data(3 downto 2);
count <= data(1 downto 0);
end if;
  end process;
end Behavioral;
Síncrono para a Maquina
De estados funcionar....

---
Com Sinais de Entrada
- Contador com uma entrada A
- Se A=0, contar 0,1,2,3,0,1,2,3,.....
- Se A=1, contar 3,2,1,0,3,2,1,0,....
a/2
!a/0
!a/2
!a/1
a/0
a/1
!a/3
a/3

---
Com Sinais de Entrada
a/2
!a/0
!a/2
!a/1
a/0
a/1
!a/3
a/3
Tabela ???
4 estados, 1 entrada, 2 bits de saida

---
Com Sinais de Entrada
a/2
!a/0
!a/2
!a/1
a/0
a/1
!a/3
a/3
A Estado Proximo Saida
0 00 01 0
0 01 10 1
0 10 11 2
0 11 00 3
1 00 11 3
.....

---
Com Sinais de Entrada
a/2
!a/0
!a/2
!a/1
a/0
a/1
!a/3
a/3
Estado A Proximo Saida
  00 0 01 0
  00 1 11 3
  01 0 10 1
  01 1 00 0
  10
.....

---
Circuito com entrada
ROM
8 palavras de
4 bits
entrada
Saida
FF

---
Ex4 teste 2011
A com 1 bit
A=0 fazer 0,2,1,3,0,2,1,3
A=1 fazer 0,1,0,1,.....

---
Ex4 teste 2011
a
!a
!a
!a
a
!a
A com 1 bit
A=0 fazer 0,2,1,3,0,2,1,3
A=1 fazer 0,1,0,1,.....